## Slide 1
李唯愷 Wei-Kai Lee Ph.D.
Postdoctoral Research Fellow
Institute of Biophotonics,
National Yang Ming Chiao Tung University, 155 Li-Nong St.,Sec.2,Taipei,Taiwan 112
Tel: 0978073290
Email: l850818@gmail.com
Education
Bachelor Degree (09/2014-06/2018)
Department of Biomedical Imaging and Radiological Sciences, National Yang-Ming University, Taipei, Taiwan
Ph.D. Degree (08/2019-08/2022)
Department of Biomedical Imaging and Radiological Sciences, National Yang Ming Chiao Tung University, Taipei, Taiwan
Experience
Postdoctoral Research Fellow (09/2022-)
Institute of Biophotonics, National Yang Ming Chiao Tung University, Taipei, Taiwan
Clinical Attachment (07/2017-01/2018)
Department of Radiology, Nuclear medicine, Radiation Oncology, Taipei veterans General Hospital
Publication:
Lee, W. K., Yang, H. C., Lee, C. C., Lu, C. F., Wu, C. C., Chung, W. Y., ... & Wu, Y. T. (2023). Lesion delineation framework for vestibular schwannoma, meningioma and brain metastasis for gamma knife radiosurgery using stereotactic magnetic resonance images. Computer Methods and Programs in Biomedicine, 229, 107311.
Lee, CC.*, Lee, WK.*, Wu, CC. et al. Applying artificial intelligence to longitudinal imaging analysis of vestibular schwannoma following radiosurgery. Sci Rep 11, 3106 (2021). *: equal contribution
Hermann I, Martínez-Heras E, Rieger B, Schmidt R, Golla AK, Hong JS, Lee WK, Yu-Te W, Nagtegaal M, Solana E, Llufriu S, Gass A, Schad LR, Weingärtner S, Zöllner FG. Accelerated white matter lesion analysis based on simultaneous T1 and T2∗ quantification using magnetic resonance fingerprinting and deep learning. Magn Reson Med. 2021 Feb 5. doi: 10.1002/mrm.28688. Epub ahead of print. PMID: 33547656.
Huai-Che Yang, Chih-Chun Wu, Cheng-Chia Lee, Huai-En Huang, Wei-Kai Lee, Wen-Yuh Chung, Hsiu-Mei Wu, Wan-Yuo Guo, Yu-Te Wu, Chia-Feng Lu, Prediction of pseudoprogression and long-term outcome of vestibular schwannoma after Gamma Knife radiosurgery based on preradiosurgical MR radiomics, Radiotherapy and Oncology, Volume 155, 2021, Pages 123-130, ISSN 0167-8140.
Wei-Kai Lee*, Chih-Chun Wu*, Cheng-Chia Lee, Chia-Feng Lu, Huai-Che Yang, Tzu-Hsuan Huang, Chun-Yi Lin, Wen-Yuh Chung, Po-Shan Wang, Hsiu-Mei Wu, Wan-Yuo Guo, Yu-Te Wu. Combining analysis of multi-parametric MR images into a convolutional neural network: precise target delineation for vestibular schwannoma treatment planning. Artificial Intelligence in Medicine, 107:101911, 2020. *: equal contribution

## Slide 2: Purpose: DICOM RT Contours Export
Acquire the MR image data and annotation of the targets at the MR images from DICOM file  Annotation also call contour, pixel label, or ROI (Region of Interest)
Pixel label
MR image

## Slide 3: Outline
Digital Imaging and Communications in Medicine, DICOM
How to decode the DICOM files
How to extract the annotations from DICOM files

## Slide 4: DICOM
Digital Imaging and Communications in Medicine, DICOM
All the equipment related to medical imaging must follow the DICOM format, include X-ray, CT, MR, RT…
Component:
  Tags (header): ID, Age, Gender,…
  2D array (pixel data)
Support:
  X-ray
  Computed Tomography, CT
  Magnetic Resonance Imaging, MRI
  Radiotherapy Structure Set, RTSS
Website: https://www.dicomstandard.org/

## Slide 5: DICOM Viewer
RadiAnt DICOM VIEWER
https://www.radiantviewer.com/

## Slide 6: DICOM
DICOM Standard Browser: interpret the tag ID, header description, usage and the value
https://dicom.innolitics.com/ciods

## Slide 7: Decode the DICOM files
Python: pydicom
  dicom_ds=dcmread(dicom filename)read dicom header and image
  dicom_ds.PixelData, dicom_ds.pixel_array (recommand) extract image array
MATLAB:
  dicominfo: read header
  dicomread: read image
C++:
  ITK library

## Slide 8: Decode the DICOM files
MATLAB: dicom=dicominfo(filename)
Python: dicom=pydicom.dcmread(filename)

## Slide 9: Purpose: DICOM RT Contours Export
Acquire the MR image data and annotation of the targets at the MR images from DICOM file  Annotation also call contour, pixel label, or ROI (Region of Interest)
Pixel label
MR image

## Slide 10: Roadmap
Read the DICOM RTSS file and confirm the modality
Identify the desired contour structures and acquire the contour data from DICOM RTSS
Identify which MR image the contour data allocate at
Convert the contour data from reference coordinate system to pixel location

## Slide 11: Roadmap
Read the DICOM RTSS file and confirm the modality
Identify the desired contour structures and acquire the contour data from DICOM RTSS
Identify which MR image the contour data allocate at
Convert the contour data from reference coordinate system to pixel location

## Slide 12: Radiotherapy Structure Set, RTSS
One of the DICOM formats
The software for radiotherapy must follow the DICOM RT format  treatment planning software, e.g. Eclipse, RapidPlan
Contents:
  Patient Name
  Age, Gender
  Lesion contours for radiotherapy
  Organ contours for dose-planning
No image data was saved in RTSS
https://www.varian.com/zh-hant/products/radiotherapy/treatment-planning/eclipse

## Slide 13: Read the DICOM RTSS and confirm the modality
Subject:
  Patient with GBM in VGHTC
Imaging Modality:
  MR imaging
Annotation Modality:
  Varian system
DICOM files: MR images
(Slice/切面)
DICOM file: Radiotherapy Structure Set

## Slide 14: Read the DICOM RTSS and confirm the modality
Platform:
  MATLAB
  dicom=dicominfo(DICOM RTSS filename)
Confirm the modality
MR images
Radiotherapy structure set, RTSS

## Slide 15: Roadmap
Read the DICOM RTSS file and confirm the modality
Identify the desired contour structures and acquire the contour data from DICOM RTSS
Identify which MR image the contour data allocate at
Convert the contour data from reference coordinate system to pixel location

## Slide 16: Identify the structure
Find the contour structures:
  dicom.StructureSetROISequence
  Obtain the ROI name to identify the correct ROI
Three contour structures were saved in this DICOM RTSS file.

## Slide 17: Acquire the contours of the desired structure
Find the contour sequence of structures:
  dicom.ROIContourSequence
  dicom.ROIContourSequence.Item_1.ContourSequence
Three contour data were saved in this DICOM RTSS file.
Multiple close planar ROI items
e.g. different close planar ROI items at different images or items at same image.
Close planar ROI

## Slide 18: Acquire the contours of the desired structure
Find the contour data from sequence:
  dicom.ROIContourSequence.Item_1.ContourSequence. Item_1.ContourData

## Slide 19: Roadmap
Read the DICOM RTSS file and confirm the modality
Identify the desired contour structures and acquire the contour data from DICOM RTSS
Identify which MR image the contour data allocate at
Convert the contour data from reference coordinate system to pixel location

## Slide 20: Identify the contour data allocate at
Read the DICOM MR image file
  dicom=dicominfo(DICOM image filename)
DICOM MR image UID
  dicom.SOPInstanceUID
DICOM files: MR images
DICOM file: Radiotherapy Structure Set

## Slide 21: Identify the contour data allocate at
Find the image UID from sequence:
  dicom.ROIContourSequence.Item_1.ContourSequence. Item_1.ContourImageSequence.Item_1.ReferenceSOPInstanceUID

## Slide 22: Acquire the contour data and located image
X coordinate
Y coordinate
Z coordinate
unit: millimeter
The coordinate is not the pixel location!
Contour data
Located image UID

## Slide 23: Roadmap
Read the DICOM RTSS file and confirm the modality
Identify the desired contour structures and acquire the contour data from DICOM RTSS
Identify which MR image the contour data allocate at
Convert the contour data from reference coordinate system to pixel location

## Slide 24: Reference coordinate system, RCS
https://itk.org/Wiki/Proposals:Orientation
RCS in patient direction:
  X-axis: right  left
  Y-axis: anterior  posterior
  Z-axis: inferior  superior
Also known as LPS orientation
X
Y
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 0 | 0
Pixel array
unit: millimeter

## Slide 25: Reference coordinate system, RCS
https://nipy.org/nibabel/dicom/dicom_orientation.html
Transform from pixel location to RCS
RCS coordinate=M*Pixel location
Obtain from the header of the located image

## Slide 26: Convert the RCS coordinate to pixel location
RCS coordinate=M*Pixel location  M-1*RCS coordinate=Pixel location
X coordinate
Y coordinate
Z coordinate
unit: millimeter
The coordinate is RCS coordinate
M-1
Column index
Row index
Slice index (optional)
Pixel location
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 0 | 0
Pixel array
Polygon to mask
0 | 0 | 1 | 0
0 | 1 | 1 | 1
0 | 0 | 1 | 0
0 | 0 | 0 | 0
Pixel label

## Slide 27: Flowchart of contour export from RTSS
Confirm the modality of DICOM file is RTSS
Radiotherapy structure set, RTSS
Identify the desired structure
StructureSetROISequence
Acquire the contours of the desired structure
ROIContourSequence
Obtain contour data (ContourData) and located image UID (ContourImageSequence.ReferencedSOPInstanceUID) from different items
X coordinate
Y coordinate
Z coordinate
M-1
Column index
Row index
Slice index (optional)
Pixel location
RCS coordinate
Construct the transformation matrix M by using the information inside the located image
M
ImagePositionPatient
ImageOrientantationPatient
PixelSpacing
Pixel array
Polygon to mask
Pixel label
1
2
3
4
5
6
7

## Slide 28: Purpose
Acquire the MR image data and annotation of the targets at the MR images from DICOM file  Annotation also call contour, pixel label, or ROI (Region of Interest)
Pixel label
(binary mask)
MR image

## Slide 29
Thanks for your attention!
Q&A

## Slide 30: Reference coordinate system, RCS
https://nipy.org/nibabel/dicom/dicom_orientation.html
The different series images in same study principally have same RCS
Construct the affine matrix M from DICOM header
Usage of M: transform the pixel location to RCS

## Slide 31: Reference coordinate system, RCS
https://nipy.org/nibabel/dicom/dicom_orientation.html
Image Position: Sx/ Sy/ Sz  upper left hand corner of the image
Image Orientation: Xx\ Xy\ Xz\ Yx\ Yy\ Yz
X
Y
X1
Y1
X1
Y1
RCS origin
[Sx Sy Sz]